## Slide 1
Overview of the Novation SL-MK3 Extension
The SL-MK3 offers an “InControl” mode and protocol that allows DAWs and programs like GigPerformer to utilize the displays and controls at a granular level. This extension works with the SL-MK3 when enabling “InControl” mode using the “InControl” button on the SL-MK3.
Control Organization
The SL-MK3 extension works with control surface items in groups by type: knobs, buttons, pads, and faders.
The extension is built around the concept of “banks” of each control group. You can have multiple knob banks, pad banks, etc.
Next to each row of controls there are up/down arrows, which the extension can utilize to “bank switch” through as many banks of such controls as you care to have in your Rackspaces.
Controlling GigPerformer with the SL-MK3 Extension
Configuration of how GigPerformer interacts with the SL-MK3 is done through widgets.
On the “Advanced” tab of each GigPerformer widget there is a field called “OSC/GPScript Name”. Any widget with a name that begins with “sl_” will be examined by the extension for information about how it should be utilized by the extension.
Every button, pad, display section, and LED on the SL-MK3 can be programmed with RGB colors. Because only so much information can be attached to a knob widget, for example, the extension will often look for information on additional widgets to control how they are displayed on the SL-MK3.
Widgets utilized by this extension fall into three broad categories:
  Control Widgets – knobs, button, etc. widgets typically linked to plugin parameters or system functions
  Parameter Widgets – used primarily to determine how Control Widgets are displayed on the SL-MK3 (e.g., colors)
  Indicator Widgets – provide feedback in GP showing which banks of Control Widgets the SL-MK3 is actively controlling

## Slide 2
Control Widgets
“Control Widgets” are typically knobs, faders, buttons, etc. linked in GP to plugin parameters. To be utilized by the SL-MK3 extension the GPScript Name must conform to the following format:
sl_type_bankID_position
“sl” identifies it as a widget of interest to the SL-MK3 extension
“type” indicates which row of SL-MK3 controls the widget will be associated with. The choices are:
k = knobs
p = pads
b = buttons
f = faders
“bankID” is any arbitrary name for this group of widgets that is meaningful to you. Typical examples:
“Pan” for panning controls of a mixer plugin
“solomute” if you wanted two RGB button rows to control solo/mute on a mixer plugin
“position” must be in the range of 0 – 15 to indicate which control position the widget is linked to
Knobs and faders are numbered 0-7, buttons and pads 0-15, arranged left to right
For example, a bank of eight knob widgets you want to use to control panning in a mixer could be named:
sl_k_pan_0 sl_k_pan_1 sl_k_pan_2 sl_k_pan_3 . . . sl_k_pan_7
The bankID “pan” in this example is entirely arbitrary. I generally use bankID’s that are descriptive, but you could just as easily name your banks things like “bank1” or “xyz” if you’re so inclined.
The purpose of this bankID is so that you can select among multiple banks. You can define as many banks as you want of each control type.
The up/down arrows next to the control groups on the SL-MK3 will scroll through banks in bankID alphabetical order.

## Slide 3
Parameter Widgets
“Parameter Widgets” can be used to specify how “Control Widgets” appear on the SL-MK3. Parameter Widgets are not strictly necessary, but without them everything will appear using default colors and labels on the SL-MK3.
Parameter Widgets associated with buttons and pads control the RGB “on” and “off” colors on the SL-MK3. Parameter Widgets for knobs control the knob color, the bar color above the knob, and optionally the resolution of the knobs.
Parameter Widgets can be created at the bank level (for controlling colors of the entire bank) or at the individual widget level.
Parameter Widgets use the same general naming format as Control Widgets, but append a “p” to the “type” field.
e.g., Control Widget “sl_k_pan_0” can have an associated Parameter Widget “sl_kp_pan_0”
Parameter Widgets intended to operate at the bank level append “p” to the “type” and drop the “_position” part of the name
e.g., Parameter Widget “sl_kp_pan” would apply to all of the knobs with BankID “pan”
Individual parameter widgets take priority over bank parameter widgets if both exist
e.g., widget “sl_kp_pan” will control the default knob color for the “pan” knob bank, but widget “sl_kp_pan_3” can be used to override that color for that knob
Parameter Widgets should generally be created as Text Widgets in GigPerformer, and often should be hidden.
The information the SL-MK3 extension looks for in Parameter Widgets is:
  Caption – sets the label that will appear on the SL-MK3 display for the widget
  Fill Color – controls the “on” color of buttons/pads or the color of knobs on the display
  Outline Color – controls the “off” color of buttons/pads or the top bar color above knobs
  Knob resolution – for knob widgets you can change the resolution by appending an “_” after the label in the Caption field followed by an integer. e.g., a Caption of “Volume_1000” would result in a knob label of “Volume” and a resolution of 1000 “ticks” to move the widget from 0.0 to 1.0. The default resolution is 250.
  Note that the alpha (transparency) of the Fill and Outline color is not used by the extension. Setting the Fill and Outline alphas to zero in GigPerfomer is an alternative to hiding these widgets. This can be useful if you want to see the label on the Rackspace but not the color

## Slide 4
Indicator Widgets
“Indicator Widgets” are similar to Parameter Widgets, but instead of controlling the colors of widgets on the SL-MK3 they are used to show on the Rackspace screen which widget banks are actively being controlled by the SL-MK3.
For example, if you have three separate banks of knobs in a Rackspace (e.g., instrument parameters, reverb parameters, and pans) it can be helpful to see on the GigPerformer screen which ones are actively linked to the knobs on the SL-MK3. You can change banks using the up/down arrow keys next to the control row on the SL-MK3 and the Indicator Widgets will reflect which bank is currently active
Indicator Widgets are named with the same format as Control and Parameter widgets but with “_i” in place of the _position.
e.g., sl_k_pan_i
Indicator Widgets are generally created as Text widget, most often with the text itself being blank or with the Text Color alpha set to zero so that the text itself does not appear on the Rackspace screen.
When the bank specified is “active” the extension will set the value of the widget to 1, which will raise its visibility on the Rackspace screen. When the bank is not active the value will be set to 0.3, which will reduce its visibility. A common use of these widgets is as an outline and background behind the associated set of Control Widgets.
The Caption of Indicator Widgets for knob and button banks controls the text that appears in the label areas on the right-most display on the SL-MK3, or temporarily in the Notify area when bank switching pad banks. Text for knob and button banks appears on two lines, which should be separated in the Caption by the “_” character. e.g., a Caption of “Solo_Mute” for a button bank would show the label “Solo” next to the top row of buttons, and “Mute” next to the bottom row.
Note – GigPerformer will remember Indicator Widget values when switching between Rackspaces/Variations/etc. As a result it will remember which banks you were controlling when you last used or saved a Variation, and when you return to it those same banks will be “active” again on the SL-MK3.
Note – the background color of an Indicator Widget is used for coloring the up/down bank select arrows on the SL-MK3. If you make each bank a different color, the up/down arrows will indicate which bank is next/previous as you bank select.

## Slide 5
Additional Controls
The buttons immediately below the display are always assigned to select Rackspaces, Variations, Songs, or Songparts. You can scroll through the them using the left and right arrow keys toward the bottom left of the control surface.
Other button assignments are:
  “Play” – starts the playhead
  “Stop” – stops the playhead
  “Clear” – toggles in and out of Setlist mode
  “Grid” – toggles between displaying Rackspaces/Variation or Songs/Songparts if you are in Setlist Mode
  “Option” – toggle the SL-MK3 displays between showing Knobs and showing Pad assignments.
Fader Controls
The faders on the SL-MK3 are not motorized, which usually means that any time you change a Rackspace, Variation, Song, or Songpart the physical position of the faders may not match the widgets they are linked to.
The SL-MK3 extension uses a “catch” approach before establishing a link between an individual fader and the widget that it is controlling. The LED above each fader indicates the status of each fader. The color codes are:
  Unlit – following Rackspace/Variation/Song/Songpart change the it is unknown if the fader is in sync with the widget
  Green – the fader on the SL-MK3 is materially higher than the value of the widget
  Red – the fader is too low relative to the value of the widget
  Blue – the fader and the widget are in sync
Bank switching for faders is not currently implemented. The widget naming format still requires a BankID for faders, but only the first one encountered by the extension within a Rackspace will be controllable.

## Slide 6
Key Lights
The SL MK3 key lights can be lit to show zone assignments. Zones and their color are defined with widgets conforming to the same standard as other widgets.
The format is:
sl_zone_zoneID_0 and sl_zone_zoneID_1
The widget values map to the first and last MIDI notes of the zone. The bottom note on the 61SL-MKII is 36, which corresponds to a widget value of 28.4. You can calculate this as [note number / 127] * 100.
The fill color of the “0” widget will be used as the RGB zone color. You can create as many “zoneID” banks as you want. Each bank will be displayed with its own color.
If these widgets are linked to GP’s Midi In blocks the “0” widget should be linked to the Min Note parameter and the “1” to the Max Note parameter.
If two zones overlap the color of the key LED will be the mathematical sum of the two colors. These may not look the way you expect or want.
  Tip: if you look at the hexadecimal values of the three color channels (RGB) in the color picker, keep each of the channels below 0x80 and overlapping colors should look more like you’d expect.
  Tip: if you want complete control over the color of overlapping zones can un-link your zone widgets from the MIDI in blocks, or create separate MIDI in blocks and widgets for any overlap portions.
Note: the key light for the highest key on the 61SL-MK3 cannot be lit through this interface.